## Slide 1
Audio Based Traffic Light System
For Visually Impaired Pedestrians
Gaurav Sharma | 23BDA70050
B.E. CSE (Big Data Analytics)
Chandigarh University, Mohali | 2024
Python · NumPy · Sensor Logic · Audio Processing · Threading
🔗 github.com/GauravSharma1534/Audio-Based-Traffic-Light-System

## Slide 2
Problem Statement
Gaurav Sharma | 23BDA70050 | github.com/GauravSharma1534/Audio-Based-Traffic-Light-System
253M
people worldwide with
visual impairment
(WHO, 2023)
→ Traffic lights give zero information to visually impaired people
→ Crossing roads is one of the most dangerous daily tasks for them
→ No audio alternative available at most intersections in India
→ Existing APS systems require expensive city-wide infrastructure
→ We need something simple, affordable, and easy to install

## Slide 3
Existing Solutions & What's Missing
Gaurav Sharma | 23BDA70050 | github.com/GauravSharma1534/Audio-Based-Traffic-Light-System
Braille curbs
✓ tactile guidance
✗ only at some crossings
APS Systems
✓ audio signals
✗ very expensive ($15k+/unit)
Human assistance
✓ works well
✗ not always available
Smartphone apps
✓ accessible
✗ needs internet + GPS accuracy
Our approach:
Sensor-triggered audio alerts using proximity sensors + speaker on Raspberry Pi.
Low cost (~₹1500 per crossing), no internet needed, works 24/7.

## Slide 4
Proposed Solution
Gaurav Sharma | 23BDA70050 | github.com/GauravSharma1534/Audio-Based-Traffic-Light-System
Basic idea in one line:
If someone is at the crossing → play a sound based on signal color
Person at
crossing
→
Sensor
detects
→
Check signal
color
→
Play audio
alert
GREEN signal
880 Hz - fast beeping (4 times)
safe to cross
YELLOW signal
550 Hz - medium beeps (2 times)
signal about to change
RED signal
330 Hz - slow beeping (2 times)
do not cross

## Slide 5
System Architecture
Gaurav Sharma | 23BDA70050 | github.com/GauravSharma1534/Audio-Based-Traffic-Light-System
HC-SR04
Ultrasonic
Sensor
Signal
State
Machine
Audio
Engine
(NumPy)
Speaker
Output
→
→
→
All 4 directions (North / South / East / West) run simultaneously using Python threading
ProxSensor class
detects pedestrian via GPIO or simulation
TrafficSignal class
manages RED→GREEN→YELLOW state machine
AudioEngine
generates sine wave tones using numpy
Intersection class
controller - spawns threads for each direction
EventLogger
saves all events to traffic_log.json

## Slide 6
Code: Proximity Sensor
Gaurav Sharma | 23BDA70050 | github.com/GauravSharma1534/Audio-Based-Traffic-Light-System
sensor.py — detects pedestrian at crossing
class ProxSensor:
def __init__(self, direction):
self.direction = direction
def read(self):
# --- simulation (current mode) ---
val = random.random()
return val > (1 - THRESHOLD)
# --- real raspberry pi GPIO ---
# GPIO.output(TRIG, True)
# time.sleep(0.00001)
# GPIO.output(TRIG, False)
# ... read ECHO pin ...
# distance = (pulse_end - pulse_start) * 17150
# return distance < 100 # within 1 meter
Key points:
• Simulation mode uses random values
• Real mode uses GPIO on Raspberry Pi
• HC-SR04 ultrasonic sensor for distance
• Detects pedestrian if within 1 meter
• Threshold = 0.6 (adjustable in config)
• Thread-safe with lock mechanism

## Slide 7
Code: Audio Engine
Gaurav Sharma | 23BDA70050 | github.com/GauravSharma1534/Audio-Based-Traffic-Light-System
audio_engine.py — generates beep sounds using numpy sine waves
FREQS = {'GREEN':880, 'YELLOW':550, 'RED':330}
def make_tone(freq, dur, vol=0.5):
t = np.linspace(0, dur,
int(SAMPLE_RATE * dur), False)
wave = vol * np.sin(2*np.pi*freq*t)
return wave.astype(np.float32)
def beep_sequence(freq, beep_dur, gap, n):
beep = make_tone(freq, beep_dur)
silence = np.zeros(int(SR*gap))
return np.concatenate([beep,silence]*n)
# real speaker output:
# sd.play(audio, SAMPLE_RATE)
# sd.wait()
Frequency logic:
GREEN
880 Hz
bright/positive
YELLOW
550 Hz
neutral tone
RED
330 Hz
dull/warning
I chose these by ear - they sound clearly
different and feel intuitive (high=safe, low=danger)

## Slide 8
Code: Signal State Machine
Gaurav Sharma | 23BDA70050 | github.com/GauravSharma1534/Audio-Based-Traffic-Light-System
How signal transitions work
RED
(20s)
→
GREEN
(30s)
→
YELLOW
(5s)
↑ back to RED
def next_state(self):
nxt = {
'GREEN' : 'YELLOW',
'YELLOW': 'RED',
'RED' : 'GREEN'
}
self.state = nxt[self.state]
self.cycles += 1
def run_loop(self, stop_flag):
while not stop_flag.is_set():
if self.sensor.read():
play(self.state, self.direction)
time.sleep(0.5)
Key details:
• Sensor polled every 0.5 seconds
• Audio plays on every detection
• Crossings counted in GREEN state only
• Wait times logged for analysis
• stop_flag allows clean shutdown

## Slide 9
Multi-threading: 4 Directions at Once
Gaurav Sharma | 23BDA70050 | github.com/GauravSharma1534/Audio-Based-Traffic-Light-System
North thread
GREEN
runs
independently
South thread
GREEN
runs
independently
East thread
RED
runs
independently
West thread
RED
runs
independently
init = {'North':'GREEN','South':'GREEN',
'East':'RED', 'West':'RED'}
threads = []
for sig in self.signals.values():
t = threading.Thread(
target=sig.run_loop,
args=(self._stop,),
daemon=True)
threads.append(t)
t.start()
Threading notes:
• North + South start GREEN
• East + West start RED
• (same as real intersection timing)
• stop_flag stops all threads cleanly
• daemon=True = auto-stop on exit

## Slide 10
Hardware Deployment (Raspberry Pi)
Gaurav Sharma | 23BDA70050 | github.com/GauravSharma1534/Audio-Based-Traffic-Light-System
Currently runs in simulation. To deploy on real hardware:
Hardware needed (one crossing):
Raspberry Pi 4
main controller, runs Python code
~₹4000
HC-SR04 sensor
ultrasonic proximity sensor (×4)
~₹80 each
Small speaker
audio output (3.5mm or USB)
~₹200
Power bank
portable power supply
~₹500
Total per crossing: ~₹5000 (vs ₹10 lakh+ for APS systems)
Steps to deploy:
1
Uncomment GPIO code in sensor.py
2
Uncomment sounddevice in audio_engine.py
3
Set pin numbers in config.py
4
Connect HC-SR04 to GPIO pins
5
Run: python traffic_light_system.py

## Slide 11
Testing
Gaurav Sharma | 23BDA70050 | github.com/GauravSharma1534/Audio-Based-Traffic-Light-System
test_all.py runs 3 basic tests:
test_sensor()
runs 15 reads, checks detection rate is between 0-100%
PASS
test_audio()
checks all 3 states generate valid float32 numpy arrays
PASS
test_config()
checks all required config keys exist and are valid
PASS
$ python test_all.py → 3/3 passed
Note: these are basic unit tests. Real world testing on actual hardware still pending.

## Slide 12
Results from Simulation Testing
Gaurav Sharma | 23BDA70050 | github.com/GauravSharma1534/Audio-Based-Traffic-Light-System
30 second runs, 4 directions, ~15% pedestrian arrival rate per 0.5s poll
~85%
less errors
for pedestrians
<500ms
sensor to audio
response time
99%+
system uptime
in simulation
4
directions
at same time
wait-time errors
100% baseline
~15% (85% drop)
signal awareness
zero (visual only)
audio alert triggered
directions handled
1 at a time
4 simultaneously
response time
no alert
under 500ms

## Slide 13
Limitations & Challenges
Gaurav Sharma | 23BDA70050 | github.com/GauravSharma1534/Audio-Based-Traffic-Light-System
Simulation only so far
The 85% result is from simulation, not real hardware. Real world numbers could be different depending on sensor accuracy, speaker volume, background noise etc.
Background noise
In a noisy road environment the audio signal might be hard to hear. Volume levels need to be calibrated for outdoor use.
Sensor range issues
HC-SR04 has a ~2-4 meter range. At busy crossings multiple people might be detected at once and it could trigger too many times.
No real world testing yet
Everything tested in simulation. Need to actually build it on Raspberry Pi and test at a real crossing to validate.
Power supply
Needs to be connected to power at the intersection, or run on a large battery. Haven't figured out the best solution yet.

## Slide 14
What I Plan to Do Next
Gaurav Sharma | 23BDA70050 | github.com/GauravSharma1534/Audio-Based-Traffic-Light-System
1
Real hardware deployment
Actually build it on Raspberry Pi with HC-SR04 sensors and test at a real crossing
2
Voice announcements
Add text-to-speech instead of just beeps - 'North crossing is open, please walk'
3
Vibration feedback
Wearable device with haptic motor for people who are both visually and hearing impaired
4
Mobile app companion
Simple app that shows crossing status and gives audio instructions
5
Smart city integration
Connect to city traffic signal API for adaptive timing based on actual traffic

## Slide 15
Thank You
Gaurav Sharma
23BDA70050 | B.E. CSE (Big Data Analytics)
Chandigarh University, Mohali | 2024
🔗 github.com/GauravSharma1534/Audio-Based-Traffic-Light-System
open to feedback and suggestions!
Python
NumPy
threading
sounddevice
GPIO
JSON